## Slide 1: Understanding Computers
Deborah Morley Charles S. Parker
15th Edition
Copyright 2015 Cengage Learning
Today and Tomorrow
Comprehensive
Chapter 7
Computer Networks

## Slide 2: Learning Objectives
Define a computer network and its purpose.
Describe several uses for networks.
Understand the various characteristics of a network, such as
topology, architecture, and size.
Understand characteristics about data and how it travels
over a network.

## Slide 3: Learning Objectives
Name specific types of wired and wireless networking media and explain how they transmit data.
Identify the most common communications protocols and
networking standards used with networks today.
List several types of networking hardware and explain the
purpose of each.

## Slide 4: Overview
This chapter covers:
  Computer network is defined
  Common networking and communications applications
  Networking concepts and terminology
  Technical issues related to networks, including general characteristics of data transmission, and types of transmission media in use today
  Explanation of the various communications protocols and
networking standards
  Various types of hardware used with a computer network

## Slide 5: What Is a Network?
Network
  A connected system of objects or people
Computer network
  A collection of computers and other hardware devices connected together so users can share hardware, software, and data, and electronically communicate
Computer networks are converging with telephone and other communications networks
Networks range from small private networks to the Internet
In most businesses, computer networks are essential

## Slide 6: Inside the Industry Box
Wireless Power
Powers/recharges devices via wireless signals and
magnetic induction
Wireless Power Consortium supports the Qi standard
Can use built-in or
external charging receiver
May be built into walls, homes, cars, garage floors, etc. in the future

## Slide 7: Networking Applications
The Internet
  Largest computer network in the world
Telephone Service
  POTS Network
    One of the first networks
    Still used today to provide telephone service to landline
phones
  Mobile Phones (wireless phones)
    Use a wireless network for communications

## Slide 8: Networking Applications
Cellular (cell) Phones
  Must be within range of cell tower to function
Dual-mode Phones
  Allow users to make telephone calls using more than one communications network
  Cellular/Wi-Fi dual-mode phones can switch seamlessly between the Wi-Fi network and a cellular network
Satellite Phones
  Communicate via satellite technology
  Most often used by individuals such as soldiers, journalists, wilderness guides, and researchers

## Slide 9: Networking Applications

## Slide 10: Networking Applications
10
Television and Radio Broadcasting
  Still used to deliver TV and radio content to the public
  Other networks involved with television content delivery are cable TV networks, satellite TV networks, and private closed-circuit television systems
Global Positioning System (GPS) Applications
  Uses satellites and a receiver to determine the exact geographic location of the receiver
  GPS receivers
    Commonly used by individuals to determine their geographic location

## Slide 11: Networking Applications
GPS receivers
  Used on the job by surveyors, farmers, and fishermen
  Used to guide vehicles and equipment
  Used by the military to guide munitions and trucks, and to track military aircraft, ships, and submarines

## Slide 12: Networking Applications
Monitoring Systems
  Use networking technology to determine the current
location or status of an object
    RFID-based Systems
      Monitor the status of objects
    GPS-based Monitoring Systems
      Monitor the physical location of objects
      Vehicle and child monitoring systems
    Electronic Medical Monitors
      Home healthcare

## Slide 13: Networking Applications
Sensors are used in some monitoring systems
  Sensor networks
  Home automation (smart thermostats, etc.)

## Slide 14: Networking Applications
Multimedia Networking
  Distributing digital multimedia content, typically via a
home network
  Necessary networking capabilities are often built into devices being used
  Might need to use multimedia networking device such as a
digital media receiver or digital media streamer
  Placeshifting Content
    Allows individuals to view multimedia content at a
more convenient location, i.e., Slingbox

## Slide 15: Networking Applications
Videoconferencing, Collaborative Computing, and Telecommuting
  Videoconferencing
    Use of computers, video cameras, microphones, and networking technologies to conduct face-to-face meetings over a network
  Telepresence Videoconferencing
    A setup that more closely mimics a real-time meeting
environment

## Slide 16: Networking Applications
Collaborative Computing (workgroup computing)
  Enables individuals to work together on documents and
projects
Telecommuting
  Individuals work from a remote location (usually home) and communicate with their places of business and clients using networking technologies
  Allows for employee flexibility

## Slide 17: Networking Applications
Telemedicine
  Use of networking technology to provide medical
information and services
  Remote monitoring and consultations
  Remote diagnosis
  Telesurgery
    Robot assisted surgery where doctor’s physical location is different from the patient’s and robot’s
    Will be needed for long-term space exploration

## Slide 18
Bitcoin versus Blockchain
Currency
Bitcoin
Blockchain
Physical and virtual objects
Transactions
Business logic - Smart contracts
Ownership
Conditional relationships
Diadic transfer
Multi-party and social
Single instance / closure
Transaction chain

## Slide 19: Network Characteristics
Wired vs. Wireless Networks
  Wired
    A network in which computers and other devices are
physically connected to the network with cables
    Found in schools, businesses, and government facilities
  Wireless
    A network in which computers and other devices are connected to the network without physical cables
    Data is typically sent via radio waves
    Found in homes, schools, and businesses

## Slide 20: Trend Box
Stadium Wireless Networks
Professional sports venues are increasingly including
wireless access and other technology
Free Wi-Fi
Seat tablet holders
In-game apps
HD video boards
20

## Slide 21: Network Characteristics
Network Topologies: Indicate how the devices in the network are arranged
  Star Networks
    All networked devices connect to a central device/server
    If the central device fails, the network cannot work
  Bus Network
    Uses a central cable to which all network devices connect
  Mesh network
    Multiple connections among the devices on the network so that messages can take any of several possible paths

## Slide 22: Network Characteristics
Time (drops of water) | Distance(cm)
1 | 10,11,12
2 | 14,78,900
3 | 43,78,22
4 | 12,45,67
5 | 56,90,765

## Slide 23: Network Characteristics
Network Architectures
  Client-Server Networks
    Client
      Computer or other device on the network that requests and utilizes network resources
    Server
      Computer dedicated to processing client requests

## Slide 24: Network Characteristics

## Slide 25: Networking Media
Number of Coils | Number of PaperClips
5 | 8,5,6
10 | 23,55,678,3
15 | 1,2,3,4
20 | 45,66,78